## Slide 1: Effects of Sub-Atmospheric Pressures on the Temperature Evolution of Spark Kernels
Daniel Caplan and David Blunck, PhD.
SciTech, 8-12 January 2018
Kissimmee, Florida
GTE-07, Control ID 2795470

## Slide 2: Why Study Low Pressure Ignition?
High altitude re-ignition
Afterburner ignition
Physics of re-light envelope
sdsadfasdf
Garuda Indonesia Flight GA421 wreckage after dual engine flameout induced by inclement weather in 2002. (Aviation Accidents, [5])

## Slide 3: How is Ignition Studied?
3

## Slide 4: Numerical Modeling
Modeled spark kernel in a cross flow of air. (Sforzo et al., [2])
Another Modeling Example

## Slide 5: Minimum Ignition Energy (MIE)
MIE Test Rig. (Anko, [3])
MIE Graphical Representation (asdfadsf, [4])

## Slide 6: Spark Kernels: Reacting
Chemiluminescence
OH* PLIF
Chemiluminescence and OH* Planar Laser Induced Fluorescence (PLIF) images of spark ignition in a piston engine. (Karlsruhe Institute of Technology, [5])

## Slide 7: Spark Kernels: Non-Reacting
Interferogram photograph of a spark kernel shock wave in nitrogen. (Topham et al., [6])
Laser-Schlieren image of a spark kernel in a crossflow of air. (Sforzo et al. [2])

## Slide 8: The Experiment
8

## Slide 9: Goals
Spatially resolved intensities and temperatures
Effects of decreasing pressure
Possible links to ignition altitude envelope

## Slide 10: Experimental Setup
CAD images of igniter jig inside vacuum chamber
Vacuum Pump
Igniter
Mirror
Heated Back Plate
Sapphire Window
Heated Back Plate
Camera
Gas Analyzer

## Slide 11: Data Collection
Camera: FLIR SC6700
MWIR InSb Detector, 1-5 μm
Blackbody calibrated
~1500 Hz
Gas Analyzer: as;lfdkjsa;ldkfj;sadkf
H2O and CO2 concentrations
Ambient Temperature and Pressure
FLIR SC6700 IR Camera [7]
Gas Analyzer Picture

## Slide 12: Experimental Setup
Photo of chamber with igniter inside
Animate with video

## Slide 13: Deconvolution Technique
Radiation transfer equation for a participating medium:
( )
Composition
Path Length
Temperature
Pressure
Intensity = function of
Solve for temperature, measuring everything else
Spectral Intensity
Emitted Radiation
Incident Radiation

## Slide 14: Temperature Interpolation Surface
Update Plot
Built using Radcal [7]
For each combination:
Composition
Pressure

## Slide 15: Determining Path Length
Camera
Line of Sight
Reflected
Width
Axis
Depth Axis
Kernel approximated as stack of ellipsoid slices
Mirror

## Slide 16: Determining Ellipse Axes
Reflected
Line of Sight
Kernel Intensity
Edge Detection
Ellipse Axes
Align Tip
Igniter Tip
Notes: 2017_12_19, DP8, {1,1}

## Slide 17: Intensity to Temperature
Intensity image…
Temperature imge…

## Slide 18: Technique Evaluation
Percentages Plot

## Slide 19: Results
19

## Slide 20: Kernel Intensities
1.0 atm video
0.6 atm video
0.3 atm video
decreased radiation emissions
shorter detectable duration
Increased bifurcation frequency
more material ablation
At Lower Pressure:

## Slide 21: Kernel Temperatures
1.0 atm video
0.6 atm video
0.3 atm video
Lower temperatures
sdsdfa
At Lower Pressure:

## Slide 22: Phase Average Temperature
1.0 atm

## Slide 23: Phase Average Temperature
0.6 atm

## Slide 24: Phase Average Temperature
0.3 atm

## Slide 25: Average Temperature
1.0 atm
0.6 atm
0.3 atm

## Slide 26: Kernel Averages
Update Plots:
Line/marker styles and colors
Font sizes
Data

## Slide 27: Summary and Conclusions
At lower pressures:
Radiation emissions are lower.
Temperatures are lower.
There is more material ablation.

## Slide 28: Acknowledgements
Air Force Research Laboratory (Craig Neuroth) for use of igniter equipment
Oregon State University for funding
OSU Propulsion Laboratory (Jonathan Bonebrake and Nathan Schorn) for use of the vacuum chamber
Chad Higgins for use of the gas analyzer
Bryan Cmelak and Tyler Castile for help with manufacturing and data collection

## Slide 29: Sources
[1] http://www.aviation-accidents.net/garuda-indonesia-boeing-b737-300-pk-gwa-flight-ga421/
[2] Sforzo, B., Lambert, A., Kim, J., Jagoda, J., Menon, S., and Seitzman, J., “Post discharge evolution of a spark igniter kernel,” Combustion and Flame, Vol. 162, No. 1, 2015, pp. 181–190.
[3] http://anko-lab.com/en/a/apparatus-for-determination-of-minimum-ignition-energy-of-a-dust-air-mixtures
[4] http://www.exschutz.net/en/basic-information-on-explosions.html
[5] http://www.itt.kit.edu/english/323.php
[6] Reinmann, R. and Akram, M., “Temporal investigation of a fast spark discharge in hemically inert gases,” Journal of Physics D: Applied Physics, Vol. 30, No. 7, 1997, pp. 1125.
[7] Grosshandler, W. L., “RADCAL: A Narrow-Band Model for Radiation Calculations in a Combustion Environment,” 1993.
[8]